## Slide 1: Nutrient Use Efficiency and Biosolids
Dr Richard Wadsworth, Dr Ruben Sakrabani, Dr Stephen Hallett
r.a.wadsworth@cranfield.ac.uk
21st September 2015

## Slide 2: Background
Project is funded by SARIC (Sustainable Agriculture Research and Innovation Club) and NERC (Natural Environment Research Council) as an innovation not research project.
An attempt to make better use of academic knowledge in a practical, environmentally benign and economically useful way.

## Slide 3: Our aims and objectives
Identify key environmental factors that influence Nutrient Use Efficiency,
Synthesise existing knowledge to generate spatially explicit data
Consult with stakeholders to determine the best use of biosolids
Disseminate knowledge through a “Data Hub” such as LandIS.
“Best” for SARIC ≈ efficient, resilient, sustainable?
“Best” for water companies ≈ trouble free, simple?
“Best” of EA ≈ material disaggregated in pure chemicals?
“Best” for environment ≈ BATNEEC (best available technology not entailing excessive costs) or BPEO (best practical environmental option)?

## Slide 4: Nutrient Use Efficiency and Biosolids
Data mostly from experimental farms.
Data mostly small-scale and short-term (some exceptions)
Data mostly ignores management skill
Most experiments NUE of N
Most reports end by stressing importance of P
Crop uptake for at least 3 years after application of biosolids (complicates estimating the “Fertiliser Replacement Value”).
Tens of thousands of farmers have been using biosolids for decades, theoretically, there is large amounts of information on agronomic, economic and environmental effects, but …

## Slide 5: Importance of Phosphate
Phosphate is a strategically important, non-renewable, heterogeneously distributed resource
Conventional agriculture depends on imported rock Phosphate (mostly from Morocco which has >80% of economically exploitable resource)
Biosolids contain usable concentrations of Phosphate
NUE of P is generally less than N, BUT, P uptake is very dependent on:
  Soil concentration
  Chemical form of the P compound
  Whether plant growth is limited by other nutrients
  Time period over which uptake is measured (years)
Phosphate can pollute, but, leaching from biosolids can be LESS than from conventional fertilisers.

## Slide 6: Where’s the best place for biosolids?
Agronomic Need
“safe sludge matrix” allows application on many crops, but, most is on winter cereals or improved grass.
cereals ~ offtake in seed and straw
Improved grass ~ offtake in silage (usually) or hay
Soils ~ mid-point of “index 2” ~ 20 mg/l Olsen-P
Subject to constraints from:
Protected areas eg SSSI, National Parks, groundwater zones etc
Heavy metal accumulation etc
Risk of erosion and runoff etc
Economic costs etc

## Slide 7: Data Flow

## Slide 8: Where to use Biosolids
Agricultural Landbank Capacity Estimator (ALOWANCE) (developed by ADAS)
Issues:
10 km resolution
Primarily ability of agricultural land to absorb additional Nitrogen
(No measures of uncertainty / variability)
(No longer funded)
There is a more detailed version, but …
There also exist Slurry Acceptance Potential Models (based on soils, slope and climate etc)

## Slide 9: Nutrient Use Efficiency
Chart: Winter Wheat
| 50 | 100 | 150 | 200 | 250 | 50 | 100 | 150 | 200 | 250 | 50 | 100 | 150 | 200 | 250 | 50 | 100 | 150 | 200 | 250
OMF15 | 9864 | 10845 | 9981 | 11241 | 10586 | 5512 | 7127 | 7458 | 7171 | 8170 | 6461 | 9442 | 12486 | 12261 | 11936 | 2498 | 3457 | 4747 | 6192 | 6082
OMF15_deeks | 7900 | 11500 | 7000
urea | 10705 | 10783 | 11070 | 10087 | 11288 | 5557 | 7518 | 8758 | 9792 | 9440 | 8081 | 9176 | 12559 | 13066 | 12534 | 3580 | 5161 | 6205 | 7468 | 7955
urea_deeks | 9700 | 10900 | 7300
Meta-analysis suggests Biosolids and organo-mineral fertilisers slightly less effective than conventional fertilizers, but, lots of “noise” and not statistically significant.
Inter-annual variation (ie the weather) is the major source of variation.

## Slide 10: Heavy Metals eg Cd
Total atmospheric Inputs of Cd in 2011
(wet + cloud + dry)
Most of England and Wales
< 600 mg/ha/yr
Atmospheric deposition ~53% of total input to agricultural land
(Rural monitoring network previously funded by Defra)
(Note recent experiments suggest that Zn and Cu more important for soil health)

## Slide 11: National Soils Inventory Cd in Soils
Point data with a 5km spacing.
Some high values can be related to:
Past land use, (eg low quality Phosphate fertilisers on Salisbury Plain),
Pollution, (eg Avonmouth Smelter),
Geology, (eg some marine clays)
Topography (eg high rainfall areas).

## Slide 12: Monte Carlo Simulations of a Cd in Arable Soils
Crop – continuous wheat – yield 5 to 7 t/ha/yr
P2O5 requirement 28.9 to 43.1 kg/ha/yr
Assume no erosion, but some leaching
Assume objective to keep soil P more or less constant
Cd concentration in wheat 0.07 to 0.09 mg/kg DW
Cd atmospheric input 200 to 300 mg/ha/yr (wet + cloud + dry)
Runoff at 3 levels 0.15 to 0.45, 0.25 to 0.55 or 0.35 to 0.65 m/yr
Percentage P in biosolids 1.48% to 2.78% (inter-quartile range UU)
Concentration of Cd in biosolids 1.08 to 1.95 mg/kg (inter-quartile UU)
Concentration of Cd in conventional fertiliser 20 to 40 mg/kg
Conversion between P2O5 and P = 0.4364
Cd leaching depends on concentration in soil pore water
Concentration in soil pore water:
  Increases with concentration in the soil
  Decreases with soil pH (3 levels simulated 5.5, 6.5 & 7.5)
  Decreases with soil organic matter (3 levels simulated 1%, 3% & 5%)
  30 years simulation, 100 trials at each permutation of pH, OM and runoff range

## Slide 13: Monte Carlo Simulation of Cd Continuous application of Biosolids
Chart: pH
| 5.5 | 5.5 | 5.5 | 6.5 | 6.5 | 6.5 | 7.5 | 7.5 | 7.5
high runoff | 1.544 | 1.128 | -0.225 | 2.149 | 1.924 | 1.118 | 2.547 | 2.389 | 1.922
moderate runoff | 1.794 | 1.522 | 0.42 | 2.4 | 2.113 | 1.497 | 2.645 | 2.513 | 2.103
low runoff | 2.117 | 1.909 | 1.159 | 2.511 | 2.363 | 1.851 | 2.73 | 2.656 | 2.324
Symbols median of 100 trials (different organic matter contents)

## Slide 14: Monte Carlo Simulation of Cd comparison of Biosolids and conventional P2O5 fertiliser
Chart: Change in soil Cd content after 30 years continuous application
| 5.5 | 5.5 | 5.5 | 6.5 | 6.5 | 6.5 | 7.5 | 7.5 | 7.5 | 5.5 | 5.5 | 5.5 | 6.5 | 6.5 | 6.5 | 7.5 | 7.5 | 7.5 | 5.5 | 5.5 | 5.5 | 6.5 | 6.5 | 6.5 | 7.5 | 7.5 | 7.5
biosolids | 1.544 | 1.128 | -0.225 | 2.149 | 1.924 | 1.118 | 2.547 | 2.389 | 1.922 | 1.794 | 1.522 | 0.42 | 2.4 | 2.113 | 1.497 | 2.645 | 2.513 | 2.103 | 2.117 | 1.909 | 1.159 | 2.511 | 2.363 | 1.851 | 2.73 | 2.656 | 2.324
conventional | 0.709 | 0.33 | -0.95 | 1.371 | 1.111 | 0.333 | 1.756 | 1.583 | 1.103 | 1.05 | 0.679 | -0.342 | 1.558 | 1.329 | 0.709 | 1.839 | 1.698 | 1.348 | 1.306 | 1.058 | 0.306 | 1.697 | 1.551 | 1.096 | 1.948 | 1.845 | 1.574
Note Nicholson et al 2006, estimate 352 years of biosolid application to reach advisory level

## Slide 15: Change in soil pH over last 20 years (UU fields with planned application) (sample of 100 fields)
Chart: Year
| 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
s_1 | 8
s_2 | 7.8 | 5.9
s_3 | 6.4 | 5.54
s_4 | 6.3
s_5 | 6.2333 | 5.8
s_6 | 7.1 | 6.5
s_7 | 6.9 | 5.8
s_8 | 6.6 | 5.9
s_9 | 6.68 | 5.7
s_10 | 6.4 | 6.11
s_11 | 5.6 | 5.1
s_12 | 6.75 | 5.75 | 6.2

## Slide 16: Change in pH over 20 years (all UU data)
Chart: pH
| 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
lower quartile | 5.325 | 5.6 | 5.8333 | 5.65 | 5.25 | 5.9562 | 5.6 | 5.9 | 5.6 | 6 | 6 | 6.4 | 5.8312 | 5.7625 | 6.1 | 6.3292 | 6.15 | 6.6 | 6.5 | 6.2 | 6.1 | 6.4875
median | 5.6 | 5.7 | 6 | 6.2 | 5.775 | 6.2 | 6.1167 | 6.3 | 6.0333 | 6.4 | 6.4 | 6.575 | 6.3 | 6.15 | 6.45 | 6.75 | 6.6 | 6.8 | 6.8 | 6.7 | 6.6 | 6.875
upper quartile | 5.8 | 6.0892 | 6.25 | 6.325 | 6.3125 | 6.5083 | 6.5375 | 6.5 | 6.3 | 6.625 | 6.9 | 6.8417 | 6.8375 | 6.4 | 6.9 | 7.0537 | 6.8333 | 7.0625 | 7.195 | 7.27 | 6.95 | 7.2

## Slide 17: Observed Change in Cd in Soils (sample of 100 fields from UU data)
Chart: Year
| 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
NY44875775 | 0.156 | 0.156 | 0.21 | 0.27
NY51613525 | 0.10733 | 0.24
NY52673387 | 0.025 | 0.16
NY53094305 | 0.0905 | 0.139 | 0.11
NY57753400 | 0.0955 | 0.21
NY58253830 | 0.099 | 0.29
NY58443252 | 0.09 | 0.2 | 0.27
NY58633800 | 0.099 | 0.33
NY58743887 | 0.099 | 0.1
NY59003405 | 0.1395 | 0.15
NY63722734 | 0.048 | 0.15767 | 0.4
NZ12231349 | 0.248 | 0.385

## Slide 18: Observed changes in Cd (all UU data)
Chart: Cd mg/kg
| 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
lower_q | 0.4 | 0.495 | 0.646 | 0.36 | 0.48125 | 0.2925 | 0.2125 | 0.05 | 0.05 | 0.18708 | 0.2 | 0.206 | 0.19075 | 0.26056 | 0.12375 | 0.078 | 0.21 | 0.26 | 0.23 | 0.3 | 0.26 | 0.26375
median | 0.945 | 1.09 | 0.7444 | 0.64 | 0.87 | 0.35375 | 0.4805 | 0.05 | 0.05 | 0.24888 | 0.368 | 0.29875 | 0.559 | 0.3475 | 0.195 | 0.19 | 0.2775 | 0.34833 | 0.3 | 0.39 | 0.33 | 0.32417
upper_q | 1.665 | 1.71 | 1.0033 | 1.125 | 0.93125 | 0.445 | 0.49 | 0.05 | 0.1255 | 0.40075 | 0.874 | 0.49525 | 0.901 | 0.48833 | 0.22525 | 0.28125 | 0.36 | 0.88875 | 0.48375 | 0.525 | 0.51 | 0.49

## Slide 19: National Soil inventory, extrapolation
National Soils Inventory – most comprehensive record of soil chemistry
Samples at 5 km intervals
Samples not chosen to be “representative” of the local landscape
Spatial auto-correlation is low
Interpolate NSI data by using median regression against soil associations, solid and drift geology and land use.
Median regression allows direct calculation of inter-quartile range for any soil property in the NSI (carbon, pH, P-Olsen etc)
Weighted average of predictions from the 4 regression equations where the “weight” is proportional the statistical significance of each class.
Example: from “drift geology”
  class “peat” = strong support (weight) for high soil carbon
  class “clay with flints” = no support for any level of soil carbon.

## Slide 20: Example – Soil pH (median estimate)

## Slide 21: Combined data
Probability that soil pH < 5
White <25%
Green 25%-50%
Yellow 50%-75%
Blue >75%

## Slide 22: Need for Phosphate
“Safe Sludge Matrix” allows application of biosolids to many crops.
Some “unexpected” constraints on biosolids eg not allowed on organic farms, not allowed on malting barley …
Modelled 2 crops, winter cereals and improved grass.
Area suitable for the 2 crops under current climate and predicted climate in 2050
Fertiliser recommendations from RB 209.

## Slide 23: Land Suitable for Winter Cereals (increase in suitable area by 2050)

## Slide 24: P2O5 requirements Winter Wheat (RB 209, Fertiliser recommendations)
Well suited = 8t/ha = 67 kg/P2O5
Moderately suited = 6 t/ha = 50 kg
Marginal = 4 t/ha = 34 kg
“Correction” for existing soil-P concentration
Soil P index 0 or 1 = + 40 kg
Soil P index 3 or more = – 40 kg

## Slide 25: P2O5 requirements Silage & Hay
P2O5 = 141 – 3.49 * Soil_P
Suitability for improved grass = f(elevation, soil association, pH, organic matter, rainfall)
Farm Business Survey – relative area of hay v silage
RB 209 – fertiliser requirements by intensity (number of silage cuts) and soil P-index

## Slide 26: Phosphate Acceptance Maps
Combined need from Winter Wheat plus improved grass under current climate and predicted for 2050
Subject to constraints / concerns by different stakeholder groups

## Slide 27: Data Flow

## Slide 28: Qualitative assessment of attitudes towards biosolids
Stakeholder | not used | problems |  | successful
 |  | Pollution / nuisance | Poor yields | 
Individual Farmers |  |  |  |   
Food industry |  |  |  | 
NFU |  |  |  | 
General public |  |  |  | 
Fertiliser producers |  |  |  | 
Fertiliser merchants/blenders |  |  |  | 
EA / Defra |  |    |  |  
Water companies |  |   |  |   
DECC |   |  |  |  
SARIC / RC |  |   |  |  

## Slide 29: Stakeholder groups and physical constraints
Constraint | Group 1 | Group 2 | Group 3 | Group 4 | Group 5
Protected Area - pollution | * | * |  |  | 
Protected Area - biodiversity | * |  | * |  | 
Protected Area - landscape | * |  | * |  | 
Heavy metal accumulation | * |  |  | * | 
Erosion > soil formation | * |  |  | * | 
Distance transported | * |  |  |  | *

## Slide 30: Protected Areas – Pollution – (NVZ), NSA, Groundwater etc
Many multiple designations
NVZ considered a constraint on management and timing not on use.

## Slide 31: Protected Areas – Biodiversity – SSSI, NNR, SAC, SPA etc
Many areas have multiple designations eg:
SSSI + NNR + SAC etc

## Slide 32: Protected Areas – Landscape – AONB, National Parks etc
Data pending for Wales

## Slide 33: Heavy Metal Accumulation – eg Ni (Nickel)
Atmospheric deposition
Median estimate in soil

## Slide 34: Heavy metal accumulation – time to reach “Soil Screening Value”
Ni
Min(Cd, Cu, Pb, Ni, Zn)
Years to reach SSV
With continuous applications

## Slide 35: Erosion – Pan-European Soil Erosion Risk Assessment
Red areas
erosion > 1.4 t/ha/yr
(optimistic estimate of soil formation)

## Slide 36: Distance
2011 Census
Biosolids > 1km from urban areas
Biosolids < 25 km from urban areas
Urban areas > 100,000 people
Distance thresholds can be altered

## Slide 37: Combining Constraints
SSSI etc
NP’s etc
NSA’s etc
Heavy metals
Erosion
Travel

## Slide 38: Group 1 All Constraints
P2O5 kg/ha/yr
Constraints

## Slide 39: Group 2 NSA, ESA & Groundwater
P2O5 kg/ha/yr
Constraints

## Slide 40: Group 3 Biodiversity + Landscape
P2O5 kg/ha/yr
Constraints

## Slide 41: Group 4 Heavy Metals & Erosion
P2O5 kg/ha/yr
Constraints

## Slide 42: Group 5 Distance
P2O5 kg/ha/yr
Constraints

## Slide 43: Implications …
800,000 tons/year biosolids
At 3% Phosphorous
At 1kg P = 2.29 kg P2O5
~ 55,000 tons of P2O5
British Survey of Fertiliser Use (Defra, 2012)
Total P2O5 England and Wales = 140,000 tons
(down from >300,000 tons 20 years ago)
Therefore, Biosolids ~ 1/3 of P2O5 needed

## Slide 44: By Region … in 2015 … Percentage of Agronomic need that could be met by biosolids
Land suitable if the agronomic need is at least 25 kg P2O5/ha
Target is for soil to be in Index 2
NUT 1 | Equivalent P2O5 t/yr | All constraints | Protected Areas - pollution | Protected Areas – Biodiversity | Heavy metals + Erosion | Distance
North-East | 2,604 | 760 | 168 | 12 | 17 | 24
North-West | 7,077 | 140 | 108 | 27 | 26 | 33
Yorkshire+Humber | 5,303 | 202 | 115 | 24 | 22 | 31
East-Midlands | 4,550 | 54 | 42 | 17 | 18 | 18
West-Midlands | 5,625 | 60 | 41 | 16 | 16 | 21
East-Anglia | 5,879 | 126 | 104 | 34 | 35 | 42
London | 8,228 | 22329 | 1105 | 623 | 583 | 6745
south-East | 8,678 | 97 | 59 | 33 | 23 | 25
South-West | 5,316 | 67 | 44 | 12 | 9 | 12
Wales | 3,073 | 45 | 14 | 7 | 8 | 21

## Slide 45: By Region .. In 2050 (+23% biosolids + CC)
Biosolids meet fractionally more of the agronomic demand
NUT 1 | tons equiv | All | PA poll | Pa bio | HM | Dist
North-East | 3202 | 838 | 151 | 13 | 19 | 28
North-West | 8704 | 175 | 133 | 32 | 32 | 40
Yorkshire+Humber | 6523 | 226 | 130 | 28 | 25 | 35
East-Midlands | 5597 | 67 | 52 | 21 | 22 | 22
West-Midlands | 6919 | 73 | 50 | 20 | 20 | 26
East-Anglia | 7231 | 159 | 130 | 43 | 44 | 52
London | 10120 | 27465 | 1356 | 765 | 717 | 8256
south-East | 10674 | 116 | 70 | 39 | 27 | 30
South-West | 6539 | 81 | 53 | 14 | 11 | 15
Wales | 3780 | 62 | 18 | 9 | 10 | 24

## Slide 46: Summary
Application of Biosolids to land is the BPEO
A water treatment works is a Phosphate mine
There is “inertia” in water treatment systems due to; capital costs, public perception etc.
Stakeholders can be grouped depending on common interests
Under some scenarios the “land-bank” is already insufficient.

## Slide 47: Discussion Points
Where would you like future research to go?
What additional data could enhance future research?
Does your organisation “map” onto these four stakeholder groups?
Is accessing and dissemination through LandIS sufficient?